## Slide 1
Amateur Radio Technician Exam Preparation Course

## Slide 2: Amateur Radio Technician Exam Prep Course
Module 5
Amateur Radio Equipment
5.1 Modulation
5.2 Transmitters and Receivers
5.3 Digital Communications
5.4 Power Supplies and Batteries

## Slide 3: Modulation & Bandwidth
TRANSMITTER
TR SWITCH
RECEIVER
POWER SUPPLY
Transceiver
Antenna
Feed line
The Basic Radio Station
Review from previous module

## Slide 4: What Happens During Radio Communication?
Transmitting (sending a signal) …
Information (voice, data, video, commands, etc.) is converted to electronic form
The information in electronic form is added to a radio wave
The radio wave carrying the information is sent from the station antenna into space

## Slide 5: What Happens During Radio Communication? (cont.)
Receiving …
The radio wave carrying the information is intercepted by the receiving station’s antenna
The receiver extracts the information from the received wave
The information is then presented to the user in a format that can be understood (sound, picture, words on a computer screen, response to a command, etc.)

## Slide 6: What Happens During Radio Communication? (cont.)
Adding and extracting the information can be simple or complex
This makes ham radio fun … learning all about how radios work
Don’t be intimidated. You will be required to only know the basics, but you can learn as much about the “art and science” of radio as you want.

## Slide 7: Adding Information – Modulation
When we add some information to the radio wave, (the carrier) we modulate the wave
  Turn the wave on and off (Morse code)
  Speech or music
  Data
Different modulation techniques vary different properties of the wave to add the information:
  Amplitude, frequency, or phase
A signal that doesn’t carry any information is called unmodulated
Recovering the information from a modulated signal is called demodulation

## Slide 8: Continuous Wave (CW)
The simplest type of modulation is a continuous wave turned ON and OFF in a coded pattern
Morse code radio signals are called CW for that reason
Figure 5.1 — Information can be added to an RF signal by modulating the signal’s amplitude.

## Slide 9: Amplitude Modulation (AM)
In AM, the amplitude of the carrier wave is modified in step with the waveform of the information (the tone shown here)
The information is contained in the outline or envelope of the resulting signal
Recovering speech or music from the envelope of an AM signal is called detection

## Slide 10: Composite Signals – Sidebands
An actual AM signal is made up of three separate signals working together — a carrier and two sidebands
The carrier is a steady, unmodulated signal
The upper sideband or USB signal is higher in frequency than the carrier
The lower sideband or LSB signal is lower in frequency than the carrier

## Slide 11: SINGLE-SIDEBAND (SSB)
In an AM signal the carrier doesn’t carry any information
Each sideband contains a copy of the modulating signal
Only one sideband is needed to transmit the information
All of the SSB signal’s power is concentrated in the one sideband
  SSB signals are effective for long-distance and weak signal voice contacts because of the additional power
The upper sideband (USB) is used on VHF and UHF
Both USB and LSB are used on the MF and HF bands

## Slide 12: Frequency and Phase Modulation
Modes that vary the frequency of a signal to add speech or data information are called frequency modulation or FM
The frequency of an FM signal varies with the amplitude of the modulating signal
Phase modulation varies a signal’s phase instead of changing its frequency … in other words, very similar to FM
FM is the mode used by most VHF and UHF repeaters
Because of the way FM receivers work, only one signal can be received at a time. This is called the capture effect and if multiple signals are present, only the strongest will be heard in the receiver.

## Slide 13: Bandwidth of Modulated Signals
A signal can have both a frequency and a strength or amplitude
Signals are spread out over a range of frequencies (called bandwidth)
You can communicate with SSB over much longer ranges and in poorer conditions than with FM or AM, particularly on the VHF and UHF bands
For even better range, extremely narrow CW signals are the easiest for a human operator to send and receive, particularly in noisy or fading conditions
CW and SSB are considered weak signal modes because they are more effective than FM at low signal strengths

## Slide 14: Bandwidth of Modulated Signals (cont.)
If an SSB signal can use either an upper or lower sideband — which one should you use?
Ham radio has standardized on the following conventions …
  Below 10 MHz, LSB
  Above 10 MHz, USB — including all of the VHF and UHF bands
    One exception: amateurs are required to use USB on the five channels of the 60 meter band (5 MHz)

## Slide 15: PRACTICE QUESTIONS

## Slide 16: What is CW?
A type of electromagnetic propagation
A digital mode used primarily on 2-meter FM
Error correction for digital transmission using code words
Another name for a Morse code transmission
T8D09 D 5-2

## Slide 17: Which of the following is a form of amplitude modulation?
Spread spectrum
Packet radio
Single sideband
Phase shift keying (PSK)
T8A01 C 5-3

## Slide 18: What type of modulation is commonly used for VHF packet radio transmissions?
FM or PM
SSB
AM
PSK
T8A02 A 5-4

## Slide 19: Which type of modulation is commonly used for VHF and UHF voice repeaters?
AM
SSB
PSK
FM or PM
T8A04 D 5-4

## Slide 20: Which of the following is a disadvantage of FM compared with single sideband?
Voice quality is poorer
Only one signal can be received at a time
FM signals are harder to tune
FM signals are more susceptible to high SWR
T8A12 B 5-4

## Slide 21: Which type of voice mode is often used for long-distance (weak signal) contacts on the VHF and UHF bands?
FM
DRM
SSB
PM
T8A03 C 5-4

## Slide 22: Which of the following signal types has the narrowest bandwidth?
FM voice
SSB voice
CW
Slow-scan TV
T8A05 C 5-4

## Slide 23: Which sideband is normally used for 10-meter HF, VHF, and UHF single-sideband communications?
Upper sideband
Lower sideband
Suppressed sideband
Inverted sideband
T8A06 A 5-4

## Slide 24: What is one characteristic of single sideband (SSB) compared to FM?
SSB signals are easier to tune in correctly
SSB signals are less susceptible to interference
SSB signals have narrower bandwidth
SSB signals are less susceptible to high SWR
T8A07 C 5-4

## Slide 25: What is the approximate bandwidth of a typical single sideband (SSB) voice signal?
1 kHz
3 kHz
6 kHz
15 kHz
T8A08 B 5-4

## Slide 26: What is the approximate bandwidth of an FM voice signal on VHF repeaters?
Less than 500 Hz
About 150 kHz
Between 10 and 15 kHz
Between 50 and 125 kHz
T8A09 C 5-4

## Slide 27: What is the approximate bandwidth of AM fast-scan TV transmissions?
More than 10 MHz
About 6 MHz
About 3 MHz
About 1 MHz
T8A10 B 5-4

## Slide 28: What is the approximate bandwidth required to transmit a CW signal?
2.4 kHz
150 Hz
1000 Hz
15 kHz
T8A11 B 5-4

## Slide 29: Transmitters and Receivers
Usually combined into one unit called a transceiver
Give you control of frequency and mode
Generalized categories
  Mobile
  Single band
  Dual band
  All band
  Multi-mode
  Handheld or HT

## Slide 30: Single-Band Mobile
Single-band, 2 meter … good starter radio
Operates from 13.8 volts DC, requires external power supply or car battery
Requires an external antenna
Can be operated mobile or as a base station
Limited to frequency modulation (FM) and usually either 2 meters or 70 cm bands
Up to approximately 50 watts output
Typical frequencies: VHF/UHF FM

## Slide 31: Dual-Band Mobile
Same as the single-band transceiver but includes additional band(s)
Most common are 2 meter and 70 cm bands
Often includes 6 meters, 222 MHz (1.25 meters) or 1.2 GHz bands
Might have separate antenna connections for each band or a single connection for a dual-band antenna
Up to approximately 50 watts output
Typical frequencies: VHF/UHF FM

## Slide 32: Multimode Transceiver
Nearly all HF rigs are multimode
VHF multimode operates on FM plus AM/SSB/CW modes
Required for weak-signal operation on VHF/UHF
More features add complexity and cost
More flexibility will allow you to explore new modes as you gain experience (and increased license privileges)

## Slide 33: Multiband Transceiver
Covers many bands – usually refers to coverage of HF + VHF/UHF
Also covers all modes
Frequently 100 watts on HF, some power limitations on high bands (25-50 watts)
Larger units have internal power supplies, smaller units need external power supply
Some have built-in “tuners”

## Slide 34: Handheld (HT) Transceiver
Small handheld FM units
Can be single band or dual band
Limited power (usually 5 watts or less)
Includes power (battery) and antenna in one package
Often purchased as a starter rig but low power limits range
Single, dual and multiband versions (with increasing cost and complexity)
Some can receive outside the ham bands, such as aircraft, commercial FM broadcast, etc.

## Slide 35: Handheld (HT) Transceiver (cont.)
Very portable and self-contained
Internal microphone and speaker
Rubber duck antenna
Battery powered
Extra battery packs
  AA cell pack useful in emergencies
Drop-in, fast charger
Extended antenna
External microphone and speaker
Headset

## Slide 36: Side-By-Side Comparison
 | SINGLE BAND | DUAL BAND | MULTIMODE | MULTIBAND | HANDHELD
FREQUENCY AGILITY | LIMITED | MEDIUM | MEDIUM | FULL | LIMITED
FUNCTION-ALITY | LIMITED | LIMITED | FULL | FULL | LIMITED
EASE OF USE | EASY | MEDIUM | MEDIUM | DIFFICULT | EASY
PROGRAM-MING | EASY | EASY | MEDIUM | CHALLENGING | EASY/MEDIUM
POWER | LOW | LOW | MEDIUM | HIGH | LOW
COST | LOW | MODEST | HIGH | HIGH | LOW

## Slide 37: Sample Radios
DUAL BAND
HANDHELD (HT)
MULTIBAND

## Slide 38: Selecting Band, Frequency and Mode
Two functions common to all radios …
  Control of frequency and mode
  Amateurs can use many different modes … most other radio services are restricted to a single mode
For multiband radios, begin by selecting the band
Then, select a frequency within the band (called tuning)
  Uses the variable frequency oscillator (VFO) and/or keypad (directly enter frequencies)
  Memories or memory channels are used to store frequencies and modes for later recall (quickly tune to frequently used frequencies)
For multimode radios, select the mode
  SSB, AM, FM, CW, Data

## Slide 39: Transmitter Functions
Transmitter output power
  In HF rigs and radios using AM/SSB and CW, controlled by an RF power control knob
  FM handheld and mobile radios have selectable fixed power levels
Microphone gain controls the level of speech audio of SSB transmitters
  FM transmitters usually have a fixed microphone gain
Switching between receive and transmit on voice …
  Manual: Use push-to-talk (PTT) button
  Automatic: Voice-operated transmitter control circuit (VOX)
  On CW (Morse Code), use a key (an electronic keyer is faster than manual)
Use a dummy load to avoid interfering with other stations while you’re adjusting transmitter (heavy duty resistor that can absorb and dissipate output power)

## Slide 40: Spurious Signals
Excessive modulation results in distortion of transmitted speech (spurious outputs on adjacent frequencies) … called splatter
Overmodulated FM signal has excessive deviation (overdeviating)
  Usually caused by speaking too loudly into the microphone
Overmodulation of an AM or SSB signal is caused by speaking too loudly or by setting the microphone gain or speech compression too high

## Slide 41: Receiver Functions
AF Gain: Volume control (sets speaker or headphone listening level)
RF Gain: Adjusts the sensitivity of the receiver to incoming signals
Automatic Gain Control (AGC): Adjusts sensitivity to keep the output volume constant for both weak and strong signals
Squelch: Mutes the receiver’s audio output when no signal is present (eliminates continuous noise)
  Many transceivers have a monitor switch that temporarily opens the squelch to hear weak signals

## Slide 42: Selectivity and Sensitivity
Receivers are compared on the basis of two primary characteristics: sensitivity and selectivity
Sensitivity determines receiver’s ability to detect signals
  Specified as a minimum detectable signal level (in µV)
A preamplifier (preamp) is used to boost sensitivity
Selectivity is the ability of a receiver to discriminate between signals
High selectivity means that a receiver can operate properly even in the presence of strong signals on nearby frequencies

## Slide 43: Filtering and Tuning
A receiver rejects unwanted signals through the use of filters
Signals then pass through filters narrow enough (i.e., smaller bandwidth) to reject all but the desired signal
Wide filters (around 2.4 kHz) are used for SSB reception
Narrow filters (around 500 Hz) are used for CW and data mode
Multiple filters allows you to reduce noise or interference by selecting a filter with just enough bandwidth to pass the desired signal
Receiver incremental tuning (RIT … also called clarifier) is a fine-tuning control used for SSB or CW
  Allows you to tune in a station that is slightly off frequency or to adjust the pitch of an operator’s voice that seems too high or low

## Slide 44: VHF/UHF RF Power Amplifiers
RF power amplifiers can be used to increase the output power by a factor of five or more
Many VHF/UHF power amplifiers can be used on all modes (including SSB and CW … switch between modes)
  Caution 1: Be sure your antenna is capable of handling the higher power!
  Caution 2: Be sure you learn about RF exposure!

## Slide 45: Transverters
By using mixers, it is possible to convert an entire transceiver to operate on a different band
  Mixers are part of equipment called a transverter
A receiving converter mixer shifts input signals to the desired band where they are received as regular signals by the transceiver
Transverters allow one main transceiver to be used on one or more new bands

## Slide 46: PRACTICE QUESTIONS

## Slide 47: Which of the following can be used to enter a transceiver’s operating frequency?
The keypad or VFO knob
The CTCSS or DTMF encoder
The Automatic Frequency Control
All these choices are correct
T4B02 A 5-5

## Slide 48: What does an FM signal sound like when received slightly off frequency?
The audio increases in pitch
The audio decrease in pitch
There is no effect except for reduction in amplitude
The audio becomes distorted
T4B04 D 5-5

## Slide 49: What is an electronic keyer?
A device for switching antennas from transmit to receive
A device for voice activated switching from receive to transmit
A device that assists in manual sending of Morse code
An interlock to prevent unauthorized use of a radio
T4A12 C 5-7

## Slide 50: What is the function of a transceiver’s PTT input?
Input for a key used to send CW
Switches transceiver from receive to transmit when grounded
Provides a transmit tuning tone when grounded
Input for a preamplifier tuning tone
T7A07 B 5-7

## Slide 51: What is the primary purpose of a dummy load?
To prevent transmitting signals over the air when making tests
To prevent over-modulation of a transmitter
To improve the efficiency of an antenna
To improve the signal-to-noise ratio of a receiver
T7C01 A 5-7

## Slide 52: What does a typical RF dummy load consist of?
A low-voltage power supply and an AC relay
A 50-ohm non-inductive resistor mounted on a heat sink
A low-voltage power supply and a DC relay
A 50-ohm inductive reactance mounted in a shielded enclosure
T7C03 B 5-7

## Slide 53: Which of the following would cause your FM transmission audio to drop out on voice peaks?
Your repeater offset is inverted
Your FM deviation is too low
You are talking too loudly
Your transmit power is too high
T2B05 C 5-8

## Slide 54: What is the effect of excessive microphone gain on SSB transmissions?
Frequency instability
Distorted transmitted audio
Increased SWR
Sideband inversion
T4B01 B 5-8

## Slide 55: What can you do if you are told your FM handheld or mobile transceiver is over-deviating?
Talk louder into the microphone
Let the transceiver cool off
Change to a higher power level
Talk farther away from the microphone
T7B01 D 5-8

## Slide 56: What is the purpose of a squelch function?
Reduce a CW transmitter's key clicks
Mute the receiver audio when a signal is not present
Eliminate parasitic oscillations in an RF amplifier
Reduce interference from impulse noise
T2B13 B 5-8

## Slide 57: How is squelch adjusted so that a weak FM signal can be heard?
Set the squelch threshold so that receiver output audio is on all the time
Turn up the audio level until it overcomes the squelch threshold
Turn on the anti-squelch function
Enable squelch enhancement
T4B03 A 5-8

## Slide 58: Which term describes the ability of a receiver to detect the presence of a signal?
RF gain
Sensitivity
Selectivity
Total Harmonic Distortion
T7A01 B 5-9

## Slide 59: Which term describes the ability of a receiver to discriminate between multiple signals?
Discrimination ratio
Sensitivity
Selectivity
Harmonic distortion
T7A04 C 5-9

## Slide 60: What is the function of the Variable Frequency Oscillator (VFO) circuit in a transceiver?
Set the receive and transmit frequency
Provide automatic frequency control
Inject a variable frequency to allow CW reception
Generate and demodulate single sideband signals
T7A11 A 5-9

## Slide 61: Which of the following controls could be used if the voice pitch of a single-sideband signal returning to your CQ call seems too high or low?
The AGC or limiter
The bandwidth selection
The tone squelch
The RIT or Clarifier
T4B06 D 5-9

## Slide 62: What is the advantage of having a choice of receiver filter bandwidths in a multimode transceiver?
Permits monitoring several modes simultaneously by selecting a separate filter for each mode
Permits noise or interference reduction by selecting a bandwidth matching the mode
Increases the number of frequencies that can be stored in memory
Increases the amount of offset between receive and transmit frequencies
T4B08 B 5-9

## Slide 63: Which of the following receiver filter bandwidths provides the best signal-to-noise ratio for SSB reception?
500 Hz
1000 Hz
2400 Hz
5000 Hz
T4B10 C 5-9

## Slide 64: What is the function of the switch which selects either SSB or CW-FM on some VHF power amplifiers?
Change the mode of the transmitted signal
Set the amplifier for proper operation in the selected mode
Change the frequency range of the amplifier to operate in the proper segment of the band
Reduce the received signal noise
T7A09 B 5-10

## Slide 65: What can be added to the output of a transceiver to increase the transmitted output power?
A potentiometer
An RF power amplifier
An impedance multiplier
All these choices are correct
T7A10 B 5-10

## Slide 66: What device converts the RF input and output of a transceiver to another band?
High-pass filter
Low-pass filter
Transverter
Phase converter
T7A06 C 5-11

## Slide 67: Digital Communications
Why use digital modes?
Special codes and characters embedded in the stream of data allow the receiving modem to detect [and correct] errors
Amateurs have developed or adapted techniques for exchanging digital data by transforming the 1s and 0s of data into tones that are in the same frequency range as the human voice

## Slide 68: Amateur Digital Modes
Different combinations of protocols, codes, and modulation, such as SSB or FM, are used to create digital modes
Popular HF digital modes
  RTTY (radioteletype)
  PSK31 (keyboard-to-keyboard)
  FT8 and WSPR (weak signal modes)
  PACTOR or WINMOR (for Winlink messaging)
Popular VHF/UHF digital modes
  Packet radio
  B2F protocol (for Winlink)
  JT65 for moon-bounce and MSK144 for scatter paths
  IEEE 802.11 (Wi-Fi) adapted to amateur use on microwave bands
Popular Voice digital modes
  AOR and FreeDV (HF)
  D-STAR, System Fusion (C4FM), DMR, and P25 (VHF/UHF)

## Slide 69: Packet and Packet Networks
On VHF and UHF, the most common digital mode is packet radio
Data characters are transmitted in groups called packets
Frequency-shift keying (FSK) is used to transmit individual characters
Each packet consists of a header, data, and checksum
If an error is detected, the receiver automatically requests the packet be retransmitted until the data is received properly (ARQ or automatic repeat request)

## Slide 70: Keyboard-to-Keyboard Modes
Digital modes that are designed for real-time person-to-person communication are called keyboard-to-keyboard modes
Most popular on HF bands
Most are generated by computer software using a sound card and an interface to a transceiver’s audio input and output
Radioteletype (RTTY) is the oldest
Most popular is PSK31 (phase shift keying, 31 baud)
  Works very well in noisy conditions

## Slide 71: Automatic Packet Reporting System (APRS)
Uses packet radio to transmit the position information from a moving or portable station
Basically a packet radio station combined with a Global Positioning System (GPS) receiver … can transmit GPS position data
Can also transmit weather information and short text messages
A common public service application of APRS is to provide maps of station locations while they are providing real-time tactical communications

## Slide 72: Setting Up For Digital Modes
Data interfaces are connected between the transceiver’s audio inputs and outputs and the computer’s data connections (USB or COM ports) or sound card jacks. A TNC or MPC (multiprotocol controller) converts between data and audio. An audio interface isolates the computer sound card from the radio to prevent hum.
Figure 5.10 … Typical Digital Mode Set Up

## Slide 73: Setting Up For Digital Modes (cont.)
A very popular example of a “sound card mode” is FT8
If you use a sound card, you may need a digital communications interface to supply the PTT (push-to-talk) signal for keying the transmitter

## Slide 74: Gateways
Figure 5.11 … Typical Gateway Set Up
An internet gateway station is a regular digital mode station and also runs software that relays data to and from the internet. The most common example of gateway stations are APRS gateways and Winlink RMS stations.

## Slide 75: Gateways (cont.)
The gateway shown in Figure 5.11 is a special kind of digital station that provides a connection to the internet via Amateur Radio
Most gateways are set up to forward messages
All of the rules and regulations about commercial and business-related messages and communications apply to internet gateways (follow the Amateur Radio rules)

## Slide 76: PRACTICE QUESTIONS

## Slide 77: Which of the following is a digital communications mode?
Packet radio
IEEE 802.11
FT8
All these choices are correct
T8D01 D 5-11

## Slide 78: Which of the following best describes an amateur radio mesh network?
An amateur-radio data network using commercial Wi-Fi equipment with modified firmware
A wide-bandwidth digital voice mode employing DMR protocols
An amateur-radio satellite communications network using modified commercial satellite TV hardware
An internet linking protocol allowing communication through repeaters around the world
T8D12 A 5-12

## Slide 79: Which of the following operating activities is supported by digital mode software in the WSJT-X software suite?
Earth-Moon-Earth
Weak signal propagation beacons
Meteor scatter
All these choices are correct
T8D10 D 5-12

## Slide 80: Which of the following is included in packet radio transmissions?
A checksum that permits error detection
A header that contains the call sign of the station to which the information is being sent
Automatic repeat request in case of error
All these choices are correct
T8D08 D 5-12

## Slide 81: What is the role of ARQ in a transmission system?
A special transmission format limited to video signals
A system used to encrypt command signals to an amateur radio satellite
An error correction method in which the receiving station detects errors and sends a request for retransmission
A method of compressing data using autonomous reiterative Q codes prior to final encoding
T8D11 C 5-12

## Slide 82: What does the abbreviation "PSK" mean?
Pulse Shift Keying
Phase Shift Keying
Packet Sampled Keying
Power Sampled Keying
T8D06 B 5-13

## Slide 83: What kind of data can be transmitted by APRS?
GPS position data
Text messages
Weather data
All these choices are correct
T8D03 D 5-13

## Slide 84: Which of the following is an application of APRS?
Providing real-time tactical digital communications in conjunction with a map showing the locations of stations
Automatically showing the number of packets transmitted via PACTOR during a specific time interval
Providing voice over internet connection between repeaters
Providing information on the number of stations signed into a repeater
T8D05 A 5-13

## Slide 85: How are the audio input and output of a transceiver connected in a station configured to operate using FT8?
To a computer running a terminal program and connected to a terminal node controller unit
To the audio output and input of a computer running FT8 software
To an FT8 conversion unit, a keyboard, and a computer monitor
To a computer connected to the FT8converter.com website
T4A04 B 5-14

## Slide 86: What signals are used in a computer-radio interface for digital mode operation?
Receive and transmit mode, status, and location
Antenna and RF power
Receive audio, transmit audio, and transmitter keying
NMEA GPS location and DC power
T4A06 C 5-14

## Slide 87: Which of the following is one of the connections required between a computer and a transceiver to operate digital modes?
Computer “line out” to transceiver push-to-talk
Computer “line in” to transceiver push-to-talk
Computer “line in” to transceiver speaker connector
Computer “line out” to transceiver speaker connector
T4A07 C 5-14

## Slide 88: What is an amateur radio station that connects other amateur stations to the internet?
A gateway
A repeater
A digipeater
A beacon
T8C11 A 5-15

## Slide 89: Power Supplies
A solid power source is important for a clean, noise-free transmitted signal and better reception
Converts the AC input power to DC current for the radio equipment
Two main ratings:
  Output voltage
  Amount of current it can supply continuously
Radios that operate from a “12 V” supply may actually work best at the slightly higher voltage of 13.8 V typical of vehicle power systems with the engine running
If you don’t know the amount of current a radio can draw … divide output power by input voltage, then double the resulting current value and round up to the nearest amp (generally, anything above 8A will work for a 50-watt mobile rig)

## Slide 90: Power Supplies (cont.)
A supply’s output voltage changes with the amount of output current
A regulated supply uses a regulator circuit to minimize the amount of voltage change
If more than just one piece of equipment is hooked up to the supply and turned on at the same time, add all of the equipment maximum current needs together

## Slide 91: Mobile Power Wiring
Radio equipment can draw large currents when transmitting
If wire is too thin, its resistance (R) will create a voltage drop (V = I × R)
The resulting lower voltage at the radio can cause it to operate improperly (distorting output signal or creating interference)
General guidelines for mobile wiring …
  Fuse should be present in both the positive and negative leads of your radio
  Connect the radio’s negative lead to the negative battery terminal or where the battery ground lead is connected to the vehicle body
  Use grommets or sleeves to protect wiring from chafing or rubbing on exposed metal
  Don’t assume all metal is connected to the battery’s negative terminal

## Slide 92: Batteries
Batteries are made up of one or more cells
How long will a fully-charged battery power your equipment? Check out Table 5.3 (next slide) …
  Divide the energy rating in ampere-hours (Ah) by the total current needs of the equipment. Remember to use average current draw for transceivers since you won’t be transmitting all the time.
Storage batteries are often used as an emergency power source … cautions:
  Contain strong acids that can be hazardous if spilled or allowed to leak
  Can release or vent flammable hydrogen gas, that can cause an explosion
  Accidentally short-circuiting a storage battery with a tool or faulty wiring can easily cause a fire and damage the battery

## Slide 93: Table 5.3: Battery Types and Characteristics
(most common types used by hams)

## Slide 94: PRACTICE QUESTIONS

## Slide 95: Which of the following is an appropriate power supply rating for a typical 50-watt output mobile FM transceiver?
24.0 volts at 4 amperes
13.8 volts at 4 amperes
24.0 volts at 12 amperes
13.8 volts at 12 amperes
T4A01 D 5-16

## Slide 96: What type of circuit controls the amount of voltage from a power supply?
Regulator
Oscillator
Filter
Phase inverter
T6D05 A 5-16

## Slide 97: Why are short, heavy-gauge wires used for a transceiver’s DC power connection?
To minimize voltage drop when transmitting
To provide a close match to the power supply output impedance
To avoid RF interference
To minimize radiative losses in the power cable
T4A03 A 5-17

## Slide 98: Where should the negative power return of a mobile transceiver be connected in a vehicle?
At the 12-volt battery chassis ground
To the shell of the power connector
To any metal part of the vehicle
Through the transceiver’s mounting bracket
T4A11 A 5-17

## Slide 99: What hazard exists when rapidly charging or discharging an unprotected battery?
Overheating or out-gassing
Excess output ripple
Electric shock
Overvoltage
T0A10 A 5-17

## Slide 100: How can you determine the length of time that equipment can be powered from a battery?
Divide the watt-hour rating of the battery by the peak power consumption of the equipment
Divide the battery ampere-hour rating by the average current draw of the equipment
Multiply the watts per hour consumed by the equipment by the battery power rating
Multiply the square of the current rating of the battery by the input resistance of the equipment
T4A09 B 5-17

## Slide 101: Which of the following battery chemistries is rechargeable?
Nickel-metal hydride
Lithium-ion
Lead-acid
All these choices are correct
T6A10 D 5-17

## Slide 102: Which of the following battery chemistries is not rechargeable?
Nickel-cadmium
Carbon-zinc
Lead-acid
Lithium-ion
T6A11 B 5-17

## Slide 103: END OF MODULE 5